## Slide 1
Sizing FM + Change Management
Vi Network AI Platform · per the IBM SNOC TSD (20-08-26) · 15M alarms/day, H200 141GB, 3 model tiers
ASSUMPTIONS
FIXED — stated in the TSD
15M alarms/day, 1M-node topology graph (§12)
52k batch / 5 min; 500k burst in <180 s (§12)
H200 141GB, FP8 / MXFP4 on vLLM (§12, §3.7)
6 model tiers incl. VLM + E5 (§3.4.6, §3.7)
8 CHM agents, Paco / VoLTE / IP (§6.8–6.13)
Release docs quarterly / bi-annual (§5.1)
Max 5 concurrent changes per circle (§6.11)
ASSUMED — planning values to validate
70% RAN-linked → 52.5k incidents/day
35% of incidents earn a GenAI RFO
RFO = 3 turns × 6k in / 400 out tokens
CHM: 1,250 change requests/day
Release drop = 150 docs → 2,250 MOPs
Peak hour = 10% of the day → 2.4×
Alarms moved 10M → 15M/day. The TSD supersedes the August one-slide. That +50% is what pushes the heavy tier to 2.06 GPU.
DECISION POINTS
1
Route by tier, not by agent
The TSD already tiers: 120b for reasoning, Gemma for extraction, Llama 8B for MOPs. Size each, then add fractions.
2
One SLO gate per tier
Heavy: latency ≤30 s. Fast: TTFT ≤1.5 s, ITL ≤25 ms. MOP: ≤120 s — batch, it only has to land in the change window.
3
Size the estate, not one model
The TSD names six model tiers but allocates nodes for two. A pool that only fits gpt-oss-120b and E5 has nowhere to put the rest.
4
Treat MOP generation as a burst
Release docs are quarterly (§5.1): 150 docs → 2,250 MOPs in one window. A daily mean hides the only CHM spike.
5
Co-locate E5, do not dedicate it
A 0.7 GB encoder at 0.03% utilisation does not need a 141 GB card. Freeing it makes all four cards heavy-capable.
6
Measure on H200, not H100
4.8 TB/s vs 3.35 — decode is bandwidth-bound, so ITL improves ~1.43×. Capacity is 7,008 tok/s, not 6,066.
PARAMETERS THAT MOVE IT
Measured on one H200 141GB, gated per tier. GPU column is what pan-India peak demand needs.
SHAPE
TOK/S
GPU
heavy · gpt-oss-120b
6k/400
7,008
2.06
fast · Gemma 4 26B
1.5k/200
20,936
0.16
mop · Llama 3.1 8B
12k/2.5k
7,733
0.17
TOTAL at pan-India peak
2.40
WHERE THE TOKENS COME FROM
FM · alarms → RFO
398M
82%
CHM · steady state
25M
5%
CHM · release burst
60M
13%
CHM does not move the number
Pan-India it is 18% of tokens and 0.33 of a GPU. The alarm tier at 15M/day sets the fleet; CHM adds model tiers, not cards.
Notes: Left: what the IBM TSD fixes versus what we assumed — note alarms moved from 10M to 15M/day, which is what drives the heavy tier. Middle: the six sizing decisions. Right: measured capacity per model tier on H200, and where the tokens come from — note the CHM release-drop burst is larger than its steady state. The headline of this slide is that Change Management adds model tiers, not GPUs.

## Slide 2
The TSD pool: right total, wrong split
Measured demand lands on the TSD’s own 4 production H200 · but the heavy tier needs 2.06 of them, so “2 active for HA” has no headroom left
PRODUCTION GPU
4 +1 × H200
Matches the TSD total.
3 serving + 1 for N+1.
HEAVY TIER
2.06 of 3 cards
gpt-oss-120b alone, at
pan-India peak.
CHANGE MGMT
18 % of tokens
Pan-India, on a release
burst day. 0.33 GPU.
THE E5 CARD
0.03 % utilised
A 0.7 GB encoder on a
141 GB card.
HA POSTURE AT PAN-INDIA PEAK
3 cards healthy
48% of knee
comfortable — the normal state
2 active (TSD HA)
72% of knee
meets SLO, 30% headroom spent
1 surviving
145% of knee
SLO breach at peak hour
Free the E5 card
4 heavy-capable
turns 2-at-the-edge into 3-with-margin
Model tiers covered
2 of 6
Gemma, Llama 8B and the VLM have no node
CHM adds tiers, not cards
CHM is 18% of tokens and 0.33 of a GPU. What it really adds is two more model tiers to host — Llama 3.1 8B for MOP generation and heavier use of the Gemma fast tier — neither of which has a node in the §12 pool.
The §12 pool covers 2 of 6 models
It allocates nodes for gpt-oss-120b and E5. Gemma 4 26B, Gemma 4 E4B, Llama 3.1 8B and the VLM are named elsewhere in the TSD with no allocation. Weights co-reside in 107 of 141 GB — but compute does not.
Reallocate rather than buy more
E5 runs at 0.03% of one card. Co-locate it with the fast tier and all four cards become heavy-capable — the same spend, but three active at peak instead of two at the edge.
Method: 13 GuideLLM operating points across the three model tiers the TSD names, calibrated to H200 141GB (4.8 TB/s — decode ~1.43× an H100, prefill held flat). Volumes are the TSD’s own: 15M alarms/day and 8 CHM agents, with FM and Change Management both dimensioned pan-India. The one thing arithmetic cannot settle is co-resident compute — that needs a run on the real card.
Notes: The total in the TSD is right — 4 production H200 — and my independent measured model lands on the same number. The issue is the split: 3 cards for gpt-oss-120b and 1 dedicated to E5 leaves the heavy tier at 2.06 of 3, so the stated 2-active HA posture has no headroom. Freeing the E5 card fixes it at zero extra cost. Lead with the middle finding in a design review: four of the six model tiers the document describes have no node allocated.